## Slide 1: Packet Radio
Greg Kruckewitt, ARRL Sacramento Valley District 3 EC

## Slide 2: Topics
Introduction
What is Packet Radio?
Why use Packet Radio?
Building a Packet Station
Software for Sending Packet Messages
Demo

## Slide 3: What is Packet Radio?
Amateur Packet Radio is one of many digital modes that Hams can use to build wireless computer networks
Packet establishes a “private connection” between two stations while sharing a frequency with other stations
Packet can use Bulletin Board Systems (BBSs) for dropping off and retrieving messages between users
You can take advantage of packet nodes to connect to distant stations

## Slide 4: How Packet Radio Works
Packet Radio uses the AX.25 protocol
Sends packets (an envelope + payload)
  Envelope contains the header at the beginning and a checksum at end
  Header contains addressing information (to, from)
  Checksum determines if packet is error-free
  Payload contains the data to be sent

## Slide 5: Packet – Making Connections…

## Slide 6: Advantages of Packet Radio?
Messages sent to a BBS can be stored and forwarded throughout connected BBS networks.
The recipient does not need to be on-line to get the message, meaning that messages can be retrieved at the recipient's convenience. This can save computer’s battery power.

## Slide 7: Advantages of Packet Radio?
Packet radio is ideal for sending complex messages
  passing lists of material, addresses, instructions, or complex words (i.e. pharmaceuticals or chemicals) You would not want to mistake Hydrogen Sulphide (a gas) with Hydrogen Sulfate (an acid)
  Error checking insures that messages are sent error-free

## Slide 8: Complex Data Sent from Tevis Ride

## Slide 9: Building a Packet Station
To build a packet station you will need:
  Computer
  Terminal Node Controller
  Radio
  Cables from computer to TNC and from TNC to radio

## Slide 10: Packet Radio Software
Terminal program
RMS Express
Outpost Packet Manager

## Slide 11: Terminal Program
Terminal programs can be used to connect and send short packet messages
Many commands to learn
Can be used for keyboard to keyboard messaging

## Slide 12: RMS Express
Designed to be used with exclusively Winlink Email System
Cannot be used to connect to a BBS or PBBS
Ideal to send email anywhere in the world
Can send attachments such as small photos

## Slide 13: Outpost Packet Manager
Designed for ARES/RACES Emcomms by Jim Oberhofer, KN6PE specifically for ARES/RACES in Santa Clara County. Used by many ARES groups for digital communications in the US.

## Slide 14: Outpost: Message List

## Slide 15: Outpost: Read Messages

## Slide 16: Outpost: Compose a Message

## Slide 17: Why Outpost is ideal for ARES
Easy to use, e-mail like interface
Folders: Inbox, Outbox, Sent, Archive, Draft, Deleted
Address book
Automates comms with TNC/BBS – just press Send/Receive
Auto logging of all messages sent and received
Makes printing a message as simple as a click

## Slide 18: Packet Radio
Demo using Outpost to connect to:
  Another packet station (peer to peer)
  Connecting to a BBS
  Connecting to Winlink to send a packet email message

## Slide 19: Resources
  Contact information Gregory Kruckewitt, KG6SJT kg6sjt@gmail.com cell: 530-219-0611
  Outpost Packet Manager http://www.outpostpm.org/
  RMS Express & Winlink http://www.winlink.org/
  www.sacvalleyares.org Links to this presentation as well as information on packet and many other topics related to ARES.